Port expander on back
The port expander uses two 25-pin connectors. The MALE connectors are attached to the TI92 and the FEMALE connectors are attached to the Marvin unit. The pinouts given are as seen when you look DOWN ONTO THE FEMALE CONNECTOR. These connectors are positioned about an inch apart with the address connector on the left. A better description will be given when the pinouts are updated.

Data connection
NC * * ser TIP
        ser GND *
        * ser MID
        ROM Vcc *
        * $400000
        $C00000 *
        * CE RAM
        R/W *
        * D15
        D14 *
        * D13
        D12 *
        * D11
        D10 *
        * D9
        D8 *
        * D7
        D6 *
        * D5
        D4 *
        * D3
        D2 *
        * D2
        D0 *

Address connection
NC *
        * GND
        NC *
        * NC
        A20 *
        * A19
        A18 *
        * A17
        A16 *
        * A15
        A14 *
        * A13
        A12 *
        * A11
        A10 *
        * A9
        A8 *
        * A7
        A6 *
        * A5
        A4 *
        * A3
        A2 *
        * A2
        A0 *

Note: There is NO A0. This pin is reserved for lower/upper byte access, but currently not used.
Rom Slot
+-----+-----+-----+-----+-----+-----+-----+-----+-----+-----+-----+-----+-----+
|Vcc | |Vcc |D12 |D13 |D14 |D15 |Vcc |A16 |A14 |A12 |A10 |A20 |
|RAM | |ROM | | | | |ROM | | | | | |
+-----+-----+-----+-----+-----+-----+-----+-----+-----+-----+-----+-----+-----+

+-----+-----+-----+-----+-----+-----+-----+-----+-----+-----+-----+-----+-----+
|NC |CE2/ |D4 |D5 |D6 |D7 |GND |A17 |A15 |A13 |A11 |A9 |NC |
| |RAM | | | | | | | | | | | |
+-----+-----+-----+-----+-----+-----+-----+-----+-----+-----+-----+-----+-----+

* CE/ ROM: accesses 400000-5FFFFF on models with internal ROM,
        accesses 200000-5FFFFF on models with no internal ROM
CPU pinout
Pin # / What it does
1 / R6
2 / R7 used for battery level detection in the TI89
3 / R8 -"-
4 / R8 -"-
5 / LCD FS normaly a pulse every 11ms (90Hz)
6 / LCD BS normaly ~740 kHz
7 / LCD ? 50/50 45Hz
8 / LCD RS norm pulse every 88uS (11.5kHz)
9..12 / LCD data
13 / Gnd
14 / Vcc
15 / reset?
16 / CS4/ (memory at $C0 0000, note that this signal was found because of what appears a bug
17 / CE1/ (ROM at $40 0000) ; in some keypressed-detecting code, which generates a
18 / CE odd byte ; write to somewhere in this area for some keys,
19 / CE even byte ; might be bad if you use this signal for access to extra ram)
20 / R/W
21 / CE2 (RAM chip select)
22 / D1
23 / D4
24 / D10
25 / D3
26 / D9
27 / D2
28 / D8
29 / D1
30 / CE3/ (ROM at $20 000)
31..38 / A1..A8
39..40 / A18..A19
41 / Vcc
42 / Gnd
43 / D4
44 / D12
45 / D5
46 / D13
47 / D6
48 / D14
49 / D7
50 / D15
51..59 / A17..A9
60 / ? (seams to output exactly the same thing as pin 51/A17
61 / A20
62 / link out (tip) (to base of transistor in Q1)
63 / link out (ring) (to base of transistor in Q1)
64 / link in (tip) (connected to pullup resistor, connected to port via D10 and L2)
65 / link in (ring) (connected to pullup resistor, connected to port via D10 and L3)
66 / Vcc
67 / Gnd
68 / OSC2/2 used for voltage multiplier generating ~16v for the LCD
69 / pin 68 inverted used for voltage multiplier generating ~16v for the LCD
70..73 / LCD constrast LSB-MSB
74 / low=LCD on
75..80 / R0-R5
81
82 / ON key
83 / C0
84 /
85 / Gnd(?)
86 / Vcc(?)
87 / OSC 2 in
88 / C1
89 / OSC 2 out
90..91 / C2..C3
92 / OSC 1 out
93 / C4
94 / OSC 1 in
95
96..98 / C5..C7
99 / used as the input for battery level detection. (can be set to output by using 600000:6,4
100 / output-pin, controlled by $600000:7,5 used for LSB in contrast on TI-92, unused on TI-89

Rx = keyboard ROW address line
Cx = keyboard COLUMN line

I/O Ports Information

---------------------

Note:This info was mostly taken from David Ellsworth's Fargo documentation

-----------------------------------------------------------------------------

INTRODUCTION

-----------------------------------------------------------------------------

If all a computer had was its RAM and ROM, it would just be an inert box

doing invisible calculations. To connect to the outside world, computers

need I/O ports. On the TI-89/92+, these ports are used to access the keyboard,

link port, LCD, and some other hardware settings.

This text file describes how the TI-89/92+ organizes its memory, and lists all

of the known I/O ports.

Since the 68000 processor has no dedicated instructions for reading and

writing I/O ports, all I/O must be memory-mapped. This means that I/O ports

are read and written by accessing specific addresses in memory. The

addresses in the range 600000-60001F correspond to memory-mapped I/O.

Directly accessing I/O ports has its advantages and disadvantages. It is

very low-level, and gives you complete control. However, it can be a complex

process, and why reinvent the wheel? For this reason, most I/O tasks (such

as reading keys, sending and receiving through the link port, and changing

the contrast) are already handled by the TI-89/92+'s ROM.

There are some times when it is still best to directly access the I/O ports.

The TI-89/92+ is capable of recognizing several keys held down at once, but the

ROM has no built-in provision for this. When you want to read multiple keys

at once in a program, you must use direct I/O.

----------------------------------------------------------------------------

THE MEMORY MAP

----------------------------------------------------------------------------

Memory addresses are 4 bytes long (32 bits). However, the 68000 processor

has a 24 bit addressing bus. For this reason, addresses listed here in

hexidecimal will be 6 digits long.

On the TI-89, memory is mapped out as follows:

000000-1FFFFF : RAM

200000-3FFFFF : Module ROM

400000-5FFFFF : Nothing

600000-6FFFFF : Memory mapped I/O (lower 6 bits)

700000-FFFFFF : Nothing (floating bus)

On the TI-92+, memory is mapped out as follows:

000000-1FFFFF : RAM

200000-3FFFFF : Module ROM, or masked ROM if there's no module

400000-5FFFFF : Plus Module ROM

600000-6FFFFF : Memory mapped I/O (lower 6 bits)

700000-FFFFFF : Nothing (floating bus)

On the TI92 (2.1 and lower versions), memory is mapped out as follows:

000000-1FFFFF : RAM

: (exact: 1FFFF [128kB memory] 3FFFF [256kB memory])

200000-3FFFFF : Module ROM

400000-5FFFFF : Expansion ROM (TI92 2.1)

600000-6FFFFF : Memory mapped I/O (lower 6 bits)

700000-FFFFFF : Nothing

Note that, for example, the RAM range covers 2 Mb. This does not mean there

is 2 Mb of RAM; it means that any RAM accesses beyond the maximum (usually

128 kb) will wrap around to the beginning. The same goes for ROM, except

that the maximum is usually 1 Mb.

TI-89 ROMs use:

000000-03FFFF to address RAM.

200000-3FFFFF to address ROM (soldered onto the board).

600000-60001F to address I/O.

TI-92+/TI92 2.1 ROMs use:

000000-03FFFF to address RAM.

400000-4FFFFF to address ROM (Plus Module ROM).

600000-60001F to address I/O.

TI92 (1.x) ROM use:

000000-01FFFF to address RAM.

200000-3FFFFF to address ROM (Plus Module ROM).

600000-60001F to address I/O.

-----------------------------------------------------------------------------

THE I/O PORTS

-----------------------------------------------------------------------------

:RO = read-only

:WO = write-only (returns random values when read)

:RW = read/write

MSB LSB

<76543210|76543210>

:RW [600000]

<.....2..|........> = something to do with keyboard

<..5.....|........> = bits <....0> of contrast

<........|.......0> = clear: interleave RAM (allows use of 256K of RAM)

<........|.....2..> = set: generate Auto-Int 7 when memory below [000120]

: is written

:WO [600002]

<........|........> =

:WO [600004]

<........|....3...> = set: 000000..1FFFFF mapped to 200000..3FFFFF

:WO [600006]

<........|........> =

:WO [600008]

<........|........> =

:WO [60000A]

<........|........> =

:RW [60000C]

<765.3210|........> = (write) link status

<........|7...321.> = (read) link status

<........|..5.....> = (read) set: one byte receive buffer has a byte

<........|.6......> = (read) set: one byte transmit buffer is empty

:RW [60000E]

<.......0|........> = set red output, if direct port access enabled

<......1.|........> = set white output, if direct port access enabled

<.....2..|........> = read red output

<....3...|........> = read white output

<.6......|........> = enable direct port access

<........|76543210> = read a byte from the receive buffer (1 byte buffer)

<........|76543210> = write a byte to the transmit buffer (1 byte buffer)

:WO [600010]

<76543210|76543210> = Address of LCD memory divided by 8

:WO [600012]

<..543210|........> = LCD horizontal frequency (?maybe?)

: The TI ROM writes $31 to this port during

: initialization.

<........|76543210> = $100 - number of LCD scanlines

: If the number of scanlines is smaller than $80 (the

: actual height of the LCD) the display will be

: duplicated in the lower half. Decreasing the height

: darkens the LCD; increasing the height lightens the

: LCD. The TI ROM writes $80 to this port during

: initialization.

:RW [600014]

<........|........> =

:RW [600016]

<........|76543210> = Programmable rate generator. Set the timer's init-

: ial value by writing it to this port. The timer is

: incremented every 6250 clock cycles, unless it has

: a value of zero, in which case it is reset to its

: initial value. The LCD is refreshed every 16th time

: this timer is incremented.

:

: See also Auto-Ints 1 and 5 in Interrupts.txt.

:

: The incrementation rate would be exactly 1600 Hz if

: the processor's clock rate were exactly 10 MHz. In

: reality, it averages around 1400 Hz, and is depen-

: dent on battery power (among other things).

:

: The ROM sets the initial value of the timer to $B2,

: effectively giving it a period of 79 ticks. It uses

: the timer for Auto Power Down, which is set to

: occur after 6000 interrupts. If the clock rate were

: 9.875 MHz, the interrupt rate would be 20 Hz and

: countdown delay would be 5 minutes. I think it is

: safe to assume that the designers of the TI-89/92+

: intended the APD delay to be 5 minutes.

:

: For this reason, and becaues it is unlikely that

: the designers intended the clock rate to be any-

: thing other than 10 MHz, I am inclined to think

: that they chose the initial value to be $B2 instead

: of $B1 for a very particular reason: auto-int 5

: will coincide with auto-int 1 with a period of 4,

: the maximum period possible. This insures that the

: TI-89/92+ will run more smoothly than it would if the

: two interrupts coincided with a period of 2 or 1.

: If you don't understand this, don't worry -- it is

: only a matter of curiosity.

:RW [600018]

<......10:76543210> = keyboard row mask; setting a bit masks the

: corresponding row of the keyboard from being

: read by [60001B].

:RW [60001A]

<......1.|........> = ON key status (0=down, 1=up)

<........|76543210> = keyboard column mask; if a bit is clear, one or

: more keys in the corresponding column are being

: held down. Keys in rows masked by [600018] are

: ignored.

:WO [60001C]

<...43210|........> = Something to do with LCD

: The TI89/TI92+ ROM writes $21 to this port during

: initialization, and $FF when the calculator is

: turned off.

<........|....3210> = bits <4321.> of contrast

:WO [60001E]

<........|........> =

-----------------------------------------------------------------------------

THE KEYBOARD MATRIX

-----------------------------------------------------------------------------

As was hinted in the I/O ports section, the keyboard is accessed internally

as a matrix. This matrix can be read by writing [600018], pausing to

allow the I/O to recover, then reading [60001B].

Keyboard Matrix on the TI 92:

-----------------------------

Row +-------+-------+-------+-------+-------+-------+-------+-------+

V Col>| Bit 7 | Bit 6 | Bit 5 | Bit 4 | Bit 3 | Bit 2 | Bit 1 | Bit 0 |

+-------+-------+-------+-------+-------+-------+-------+-------+-------+

| Bit 0 | down | right | up | left | hand | shift |diamond| 2nd |

| Bit 1 | 3 | 2 | 1 | F8 | W | S | Z | unused|

| Bit 2 | 6 | 5 | 4 | F3 | E | D | X | unused|

| Bit 3 | 9 | 8 | 7 | F7 | R | F | C | STO |

| Bit 4 | , | ) | ( | F2 | T | G | V | space |

| Bit 5 | TAN | COS | SIN | F6 | Y | H | B | / |

| Bit 6 | P | ENTER2| LN | F1 | U | J | N | ^ |

| Bit 7 | * | APPS | CLEAR | F5 | I | K | M | = |

| Bit 8 | unused| ESC | MODE | + | O | L | theta |backspc|

| Bit 9 | (-) | . | 0 | F4 | Q | A | ENTER1| - |

+-------+-------+-------+-------+-------+-------+-------+-------+-------+

Note: ENTER1 is on the alphabetic _and_ numeric keypads.

ENTER2 is next to the cursor pad.

Keyboard Matrix on the TI 89:

-----------------------------

Row +-------+-------+-------+-------+-------+-------+-------+-------+

V Col>| Bit 7 | Bit 6 | Bit 5 | Bit 4 | Bit 3 | Bit 2 | Bit 1 | Bit 0 |

+-------+-------+-------+-------+-------+-------+-------+-------+-------+

| Bit 0 | Alpha | Diam. | Shift | 2nd | Right | Down | Left | Up |

| Bit 1 | F5 | Clear | ^ | / | * | - | + | Enter |

| Bit 2 | F4 |Backspc| T | , | 9 | 6 | 3 | (-) |

| Bit 3 | F3 |Catalog| Z | ) | 8 | 5 | 2 | . |

| Bit 4 | F2 | Mode | Y | ( | 7 | 4 | 1 | 0 |

| Bit 5 | F1 | Home | X | = | | | EE | STO | Apps |

| Bit 6 | | | | | | | | Esc |

+-------+-------+-------+-------+-------+-------+-------+-------+-------+

Because of the way the TI89/TI92+ 's keyboard is wired, if you hold down three

keys that form the corners of a rectangle, the TI89/TI92+ will think you are

also holding down the key at the fourth corner.

The [ON] key is special, and is not part of the matrix.

-----------------------------------------------------------------------------

INTERNAL ROUTINES

-----------------------------------------------------------------------------

This section contains some system routines that are used in the TI89/92+'s ROM

to perform specific tasks.

------------

Reset_Link()

------------

Wait $4E20

Mask Int 5

Read [60000C].W

[60000C].B = $E0

Wait $0100

Set bit 0 of [60000E].B

Set bit 1 of [60000E].B

Wait $0100

Clear bit 0 of [60000E].B

Clear bit 1 of [60000E].B

Wait $0100

Flush()

-------

Flush()

-------

[60000C].B = $8D

Memory upgrade
Requirements :
- 128Kx8 SRAM such as Toshiba TC551001BFL-70L in SOP32 package
- small wrapping wire
- small soldering iron
- Have the same board as I : it seems my board is not very common
BE CAREFUL : this requires a lot of patience and ability to handle very small SMD components !!!
You will need to unscrew the plastic protection cover of the TI92 (no more warranty !!!) and to ajust
some of the plastic cover parts in order to have room enough to put the additional components !!!
Connections :
(see the connector pinout)
Principle is to connect data pins D0-D7 from the new SRAM to data D8-D15 of the 68000 bus.
A0 will be connected to A17 of the 68000 bus.
A1-A16 will connect directly to A1-A16, VCC to VCC, GND to GND and CE2 to CE2.
CS1/ will be connected to CS RAM.
I did as follow : (you don't need to do the same, I assume no responsability !!!)

- I first (long ago) removed the plastic cover of the ROM module (I don't know if it is still possible to put it back
when all wires are soldered).
- I removed the backup cell and the plastic cover (many screws). Be carefull, the PCB is no more screwed !!!
- Remove the ROM module.
- I put the new SRAM over the old one and soldered directly all pin to the internal one, except D0-D7,A0 and CS1/ .
(You need to adjust the pins in order to do so, pin length is a little too short to reach the pin of the internal RAM, but
solder will do the rest !!! It is very hard to explain, and I would like to have a snapshot of my TI to explain this better).
- The remaining pins are connected using the wrapping wire to the pins at the base of the ROM connectors as shown on the above picture
- - The OE pin of the SRAM (internal, and additional, since they are linked together) is just connected to GND. (This is especially important to know if you are planning to connect the additional RAM directly of the module expansion port, instead of doing it the way I did)